Decomposition of complex reactions in constructing kinetic models

Semyon Spivak

Bashkir State University, Professor, Head of Chair Mathematical Modelling

Address: 450074, Ufa, Zaki Validi Street, 32

Office phone 8 (347) 2299635

E-mail: semen.spivak @ mail.ru

Institute of Petrochemistry and Catalysis RAS, Head of the Laboratory of Mathematical Chemistry

Albina Ismagilova

Bashkir State University, Doctoral Student in Mathematical Modeling

Address: 450074, Ufa, Zaki Validi Street, 32

Office phone 8 (347) 2299635

E-mail: ismagilovaas@rambler.ru

Neftekamsky branch of Bashkir State University, Assistant Professor

Office phone 8(34783)21710

Mobile phone +79273033355

Keywords: inverse problem, informativeness, model parameters, basis of nonlinear parametric functions, reaction route.

Abstract. This paper deals with inverse problems of chemical kinetics. Systems of non-linear ordinary differential, differential algebraic, or algebraic equations, depending on the conditions of the experiment, namely, non-stationary, stationary, or equilibrium cases, constitute the mathematical object of the study. The insufficient informativity of the actually available arrays of kinetic measurement data results in the non-uniqueness of inverse problem solution. The construction of automation systems of analysis of  informativeness is  based on the decomposition of the complex chemical system into a number of systems of considerably smaller dimension. The basis of the theory of decomposition is the theory of independent routes. Constructed algorithms are illustrated by the mechanism of synthesis of vinyl chloride on the catalyst «sublimate-activated carbon».

References

1. Slin'ko M.G. Kinetic studies - the basis of mathematical modeling of chemical processes and reactors. Kinetika i kataliz [Kinetics and Catalysis], 1972, v.13, no. 3, pp.566-580 (in Russ.).

2. Spivak S.I., Timoshenko V.I., Slin'ko M.G. Methods of kinetic modeling of steady-state reactions. Kinetika i kataliz [Kinetics and Catalysis], 1972, v.13, no 6, pp.1570-1578 (in Russ.).

3. Klibanov M.V., Spivak S.I., Slin'ko M.G., Timoshenko V.I. On the number of independent parameters of stationary kinetic model. Doklady AN SSSR [Doklady AS of the USSR], 1973, v.208, no 6, pp.1387-1390 (in Russ.).

4. Yablonsky G.S., Spivak S.I. Mathematical models of chemical kinetics. M.: Znanie, 1977 (in Russ.).

5. Spivak S.I., Gorsky V.G. On the completeness of the available kinetic measurements in determining the rate constants of complex chemical reactions. Himicheskaya Fizika [Chemical Physics], 1982, v.1, no 2, pp.237-243 (in Russ.).

6. Katzman E.A. Experimental determination of kinetic and thermodynamic parameters of complex chemical reactions and numerical analysis of identifiability: Author. ... Doc. chem.sciences. Moscow, 2008 (in Russ.).

7. Temkin M.I. Mechanism and kinetics of complex catalytic reactions. Lectures given at the first symposium of the International Congress on Catalysis. M.: Nauka, 1970, pp. 57-76 (in Russ.).

8. Temkin O.N. Kinetic models of multipath reactions in homogeneous metal complex catalysis. Kinetika i kataliz [Kinetics and Catalysis], 2012, v.53, no 3, pp. 326-357 (in Russ.).

9. Volpert A.I., Khudyaev S.I. Analysis in classes of discontinuous functions and equations of mathematical physics. M.: Nauka, 1975, 394 p.

10. Spivak S.I., Ismagilova A.S., Khamitova I.A. Graph-theoretic method for determining the routes of complex chemical reactions. Doklady AN [Doklady AS], 2010, v.434, no 4, pp.499-501 (in Russ.).

11. Registration certificate of electronic resource No. 19024. Program for finding independent route of a complex chemical reaction / Akhmerov A.A., Ismagilova A.S., Spivak S.I. Registered at INIPI RAO, OFERNiO, Moscow, March 27, 2013.

12. Registration certificate of electronic resource No. 19433. Program for finding the basis of key substances / Ahmerov A.A., Ismagilova A.S. Spivak S.I. Registered at INIPI RAO, OFERNiO, Moscow, August 1, 2013.

13. Registration certificate of electronic resource No. 19737. Program for finding the basis of key substances by decomposition chemical reaction routes / Ahmerov A.A., Ismagilova A.S. Spivak S.I. Registered at INIPI RAO, OFERNiO, Moscow, December 9, 2013.

14. Spivak S.I., Ismagilova A.S. Informativeness kinetic measurements and inverse problems of chemical kinetics. Doklady AN [Doklady AS], 2013, v.451, no 3, pp. 296-298 (in Russ.).

15. Kiperman S.L. Basics of chemical kinetics in heterogeneous catalysis. M.: Khimiya, 1979, 350 p. (in Russ.).

Kinetic model is the basis of modeling of chemical processes and reactors

Bykov Valerii Ivanovich – professor, Doctor of Science (Math&Physics), Leading Researcher, Emanuel Institute of Biochemical Physics, Russian Academy of Sciences,

Address: 119334, Moscow, Kosygina st., 4

Office: +7 (499) 135 78 94

e-mail: vibykov@mail.ru

Tsybenova Svetlana Batozhargalovna – Doctor of Science (Math&Physics), professor, Department of Information Systems and Technology, Moscow City Pedagogical University

Address: 115191, Moscow, 2nd Tulskaya per, 4

e-mail: tsybenova@mail.ru

Keywords: kinetic model, parametric analysis, catalytic processes, chemical reactor

Abstract. It is known that the kinetic model is the basis for mathematical modeling of catalytic processes and reactors. At a variation of conditions of implementation of the process there is a problem of parametric analysis of the kinetic model containing a large number of parameters. Effective procedure for qualitative and numerical analysis of the relevant kinetic model is proposed. As an example a parametric analysis of Volter-Sal'nikov’s mathematical model for CSTR was performed. The dependencies of the steady states of the dimensionless parameters, the bifurcation curves of steady states, parametric and phase portraits, time dependencies were constructed.

References

- Slin'ko M.G. Fundamentals and principles of mathematical modeling of catalytic processes. Novosibirsk: Boreskov Institute of Catalysis SB RAS, 2014 (in Russ.).

- Slin'ko M.G. Kinetic model is as a basis for mathematical modeling of catalytic processes. Teoreticheskie osnovyi himicheskoy tehnologii [Theoretical Foundations of Chemical Engineering], 1976, V.10. no.1, pp. 137–146 (in Russ).

- Bykov V.I. Modelling of critical phenomena in chemical kinetics. Moscow: KomKniga, 2007 (in Russ.).

- Bykov V.I., Tsybenova S.B., Slin’ko M.G. Andronov-Hopf's bifurcation in Aris-Amundson's model. Doklady akademii nauk [Doklady Physical Chemistry], 2001. V.378. no.1. pp.214(217 (in Russ).

- Bykov V.I., Tsybenova S.B., Slin'ko M.G. The dynamics of the flow reactor partial mixing. Doklady akademii nauk [Doklady Physical Chemistry], 2001. V.380. no.5. pp.649–651 (in Russ).

- Bykov V.I., Tsybenova S.B., Slin'ko M.G. Modeling of a reaction on a catalyst surface. Doklady akademii nauk [Doklady Physical Chemistry], 2003. V.388. no.6. pp.769–773 (in Russ).

- Bykov V.I., Tsybenova S.B., Slin'ko M.G. Dangerous and safe boundaries of critical phenomena in kinetics of exothermal reactions. Doklady akademii nauk [Doklady Physical Chemistry], 2001. V.378. no.3. pp.355–358 (in Russ).

- Bykov V.I., Tsybenova S.B. Nonlinear models of chemical kinetics. Moscow: KRASAND, 2011(in Russ.).

- Volter B.V., Salnikov I.E. Stability of working regimes of chemical reactors. Moscow: Himiya, 1981 (in Russ.).

Multi-stage modeling of the combustion of a wood particle

Kolesnyk VasiliyV.

National Technical University of Ukraine (KPI), docent

E-mail: kolesnyk@email.ua

Orlyk Vladimir N.

Gas Institute of the National Academy of Sciences of Ukraine, Leading Researcher

Tel.: +380 (44) 456 03 24

E-mail: orlyk-v@mail.ru

Chumachenko Victor A.

PhD, Chemical Engineering, Senior researcher

Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences. 
pr. Lavrentieva 5, Novosibirsk, Russia, 630090.

T.: +7 (383) 32 69 412. E-mail: vachum@catalysis.ru

Keywords: mathematical model, combustion, wood particle, volatile components, burn-up time.

Abstract. The combustion of a small wood-waste particle formulated as an internal problem was considered. Such a formulation corresponds to the particle’s burning in a high-temperature gas flow enriched by oxygen. The mathematical description of heating, free and bound water removal, volatile components’ emission and combustion, carbon-residue burning were studied in details. The proposed mathematical model allows the study of the dynamics of simultaneous processes occurring in separate zones of the burning particle with time-varying boundaries. The software package developed in the course of the study may serve as a basis for investigation of the combusting processes of small wood-waste particles in real working conditions according to the chosen combustion technology.

References

1. Golovina E.S. High-temperature combustion and gasification of carbon.  Moscow: Energoatomizdat, 1983, 176 p. (Rus.)

2. Babii V.I., Serebriakova A.G., Popova I.F., Novitsky N.V., Martynova M.I. About duration of  burning Kuznetsk coal dust of grades D, F, GJ, SS, Teploenergetika [Thermal Engineering], 1977, no 1, pp.13-15 (in Russ.).

3. Demidovich B.P., Maron I.A., Shuvalova E.Z. Numerical methods of analysis.  Moscow: Fizmatgiz, 1963, 400 p. (Rus.)

4. Marchuk  G.I. Methods of Computational Mathematics. Moscow: Fizmatgiz, 1989, 608 p. (Rus.)

5. Karp I.N., Provalov A.Y., Pyanykh K.E., Yudin A.S. The Research of Sawdust and Sunflower Husks Burn-out Time Dynamic in a Fluidized Bed. Energotekhnologii i resursosberezhenie [Energotechnologii and Resources], 2010, no 3, pp. 9-13 (in Russ.).

Modeling of the methanol to formaldehyde oxidation process in multi-tubular reactor in consideration of the flow non-uniformity

Ovchinnikova Elena V.

PhD, Chemical Engineering, Senior researcher

Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences. 
pr. Lavrentieva 5, Novosibirsk, Russia, 630090.

T.: +7 (383) 32 69 412. E-mail: evo@catalysis.ru: ava@ngs.ru

Klenov Oleg P.

PhD, Chemical Engineering, Senior researcher

Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences. 
pr. Lavrentieva 5, Novosibirsk, Russia, 630090.

T.: +7 (383) 330 62 78. E-mail: klen@catalysis.ru

Vernikovskaya Nadezhda V.

PhD, Chemical Engineering, Senior researcher

Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences. 
pr. Lavrentieva 5, Novosibirsk, Russia, 630090.

T.: +7 (383) 32 69 438. E-mail: vernik@catalysis.ru

Chumachenko Victor A.

PhD, Chemical Engineering, Senior researcher

Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences. 
pr. Lavrentieva 5, Novosibirsk, Russia, 630090.

T.: +7 (383) 32 69 412. E-mail: vachum@catalysis.ru

Keywords: mathematical modelling, aerodynamic modelling, multi-tubular reactor, non-uniformity of gas flow velocity, radial heat conductivity, formaldehyde, oxide catalyst.

Abstract. The results of aerodynamic and mathematical modeling of the multi-tubular reactor for methanol to formaldehyde oxidative conversion are presented. CFD-modeling was employed with the FLUENT package and revealed the existence of significant gas flow non-uniformities in the upstream space above the catalytic tubes. Mathematical modelling of the process over Fe-Mo catalyst was performed in consideration of the actual non-uniformity factor in various tubes. This approach allows the study of the effect of uneven flow distribution on the temperature and concentration modes of reactor operation, as well as on the total reactor productivity. The obtained results are of practical interest for the analysis of industrial tubular reactor performance.

References

- http://marketpublishers.ru/lists/9519/news.html, 27.06.2014г.

- Crichton B., Formaldehyde demand. Informally speaking. A formaldehyde magazine from Formox, Spring/Summer,1212.

- Bibin V.N., Popov B.I.  Kinetics of methanol oxidation by air on the ferromolybdenum oxide catalyst. Kinetics and Catalysis, 1969,  no.6, pp.1826 (Eng. Transl.).

- Pushkaryov A.G., Arkhireev V.P., Savina T.A. Influence Fe-Mo oxide catalyst for oxidation methanol to formaldehyde on quality urea-formaldehyde concentrate. Khimicheskaya promyshlennost’ segodnya [Chemical Industry Today], 2011, no.2, pp.37-41 (in Russ.).

- Soares A.P.V., Portela M.F., Kiennemann A. Kinetics of the main and side reactions of the methanoloxidation over iron molybdates. Studies in Surface Science and Catalysis, 2001 , vol.133, pp. 489-494.

- Tatibouët J.M. Methanol oxidation as a catalytic surface probe. Applied Catalysis A: General, 1997, vol.148, no.2, pp. 213-252

- Cheng W.-H. Methanol and Formaldehyde Oxidation Study over Molybdenum Oxide, Journal of Catalysis, 1996, vol.158, no.2, pp. 477-485.

- Busca G. Infrared studies of the reactive adsorption of organic molecules over metal oxides and of the mechanisms of their heterogeneously-catalyzed oxidation. Catalysis Today, 1996, vol.27, no.3-4, pp. 457-496.

- Matros Yu.Sh. Catalytic Processes Under Unsteady-State Conditions, Elsevier, 1988, 402.P

- Ovchinnikova E.V., Chumachenko V.A., Vernikovskaya N.V., Kashkin V.N., Andrushkevich T.V. A study of nicotinic acid synthesis on a pilot installation and its simulation. Russian Journal of Applied Chemistry, 2010, vol.83, no.5, pp.846-853 (Eng. Transl.).

- KagyrmanovaA.P., ZolotarskiiI.A., VernikovskayaN.V., Smirnov E.I., Kuz'minV.A., ChumakovaN.A. Modeling of steam reforming of natural gas using catalysts with grains of complex shapes. Theoretical Foundations of Chemical Engineering, 2006,vol.40, pp.155-167

- Evenchik A.S., Makhlin V.A. Parametric sensitivity of catalytic tubular reactor. Theoretical Foundations of Chemical Engineering, 1991, vol.25, no.6, pp.828-835.

- Ovchinnikova E.V.,  Chumachenko V.A., Valuiskikh N.N. Influence of the process parameters on temperature conditions and productivity of multitubular reactor for methanol to formaldehyde oxidation. Catalysis in Industry, 2013, vol.5, no.4, pp.297-311 (Eng. Transl.).

- Makhlin V.A. Development and analysis of heterogeneous catalytic processes and reactors. Theoretical Foundations of Chemical Engineering, 2009, vol.43, no.3, pp.245-259 (Eng. Transl.).

- Informally speaking. The formaldehyde news letter from Formox, Spring/Summer, 2010.

- Fluent. Version 6.1. Fluent Inc., Lebanon, New Hampshire, 2003.

- Kagyrmanova A.P., Zolotarskii I.A., Smirnov E.I., Vernikovskaya N.V. Optimum dimensions of shaped steam reforming catalysts. Chemical Engineering Journal, 2007, vol.134, no.1-3, pp.228-234.

- Beskov V.S. Modelirovanie i optimizaciya kataliticheskih processov [Modeling and Optimization of Catalytic Processes], 1965, pp.59-67 (in Russ.).

- Nikolov V.A., Anastasov A.I. Influence of the inlet temperature on the performance of a fixed-bed reactor for oxidation of o-xylene into phtalic anhydride. Chemical Engineering Science, 1992, vol.47, pp.1291-1298

- Klenov O.P., NoskovA.S. Computational fluid dynamics in the development of catalytic reactors. Catalysis in Industry, 2011, vol.3, no.4, pp.331-349 (Eng. Transl.).

- Menshutina N.V., Gordienko M.G., Lebedev E.A., Voynovskiy А.А. Application of CFD-technique for chemical technology problems. Khimicheskaya promyshlennost’ segodnya [Chemical Industry Today], 2010, no.6, pp. 44-51 (in Russ.).

- Laptev A.G., FarakhovT.M. Ocenka dliny vhodnogo uchastka v protochnom neuporyadochennom sloe pri turbulentnom regime. Khimicheskaya promyshlennost’ segodnya [Chemical Industry Today],  2014, no.4, pp.48-52 (in Russ.).

- Smirnov E.I., Muzykantov A.V., Kuzmin V.A., Kronberg A.E., Zolotarskii I.A. Radial heat transfer in packed beds of spheres, cylinders and Rashig rings: Verification of model with a linear variation of (er in the vicinity of the wall. Chemical Engineering Journal, 2003, vol.91, pp. 243–248.

- Ovchinnikova E.V., Vernikovskaya N.V., Andrushkevich T.V., Chumachenko V.A. Mathematical modeling of (-picoline oxidation to nicotinic acid in multitubular reactor: Effect of the gas recycle. Chemical Engineering Journal, 2011, vol.176-177, pp.114–123.

- Kagyrmanova A.P., Chumachenko V.A., Korotkikh V.N., Kashkin V.N., Noskov A.S. Catalytic dehydration of bioethanol to ethylene: Pilot-scale studies and process simulation. Chemical Engineering Journal, 2011, vol.176-177, pp.188– 194.

- Ergun. S. Fluid Flow through Packed Columns. Chemical Engineering Progress, 1952, vol.48, no.2, pp.89-94.

Nonstationary  catalysis - a way to increase the efficiency of the reactions

Reshetnikov Sergey Ivanovich, Boreskov Institute of Catalysis, Siberian Branch Russian Academy of Sciences, doctor of chemical science, leading scientific researcher;

Tel. +7(383)-333-16-18

E-mail: reshet@catalysis.ru

Keywords: mathematical modelling, unsteady state of the catalyst,  reaction kinetics

Abstract. On the basis of the the simple kinetic model of a selective reaction that assumes two types of active sites, the performance of the dual-reactor system with the catalyst circulating between reactors under unsteady state conditions was analyzed theoretically. The main parameters affecting the state of the catalyst are the temperature and the rate of catalyst circulation between the zones.

The catalytic oxidation of o-xylene to phthalic anhydride in a fluidized-bed reactor was simulated. The mathematical model implies that reactor was divided into two zones by a height, and the catalyst was circulated between the zones. It is shown that the regulation of the unsteady state condition of the catalyst by means of its circulation between zones allows considerable increasing the yield of the target product.

References

1. Silveston P., Ross R.R. and Renken A. Periodic operation of catalytic reactors – introduction and overview. Catalysis Today, 1995, no. 25, pp. 91-112.

2. Silveston P.S. Composition modulation of catalytic reactors: Gordon and Breach Science Publishers: 1998.

3. Boreskov G.K. and Matros Yu.Sh. Unsteady-state performance of heterogeneous catalytic reactors. Catal. Rev.-Sci. Eng, 1983, no.4, pp.551-590.

4. Renken A. Unsteady-state operation of continuous reactors. Int. Chem. Eng, 1984,

vol.24, pp.202-213.

5. Contractor R.M. Garnett D.I., Horomvitz H.D. et. al. A new commercial-scale process for n-butane oxidation to maleic anhydride using a circulating fluidized-bed reactor . Stud. Surf. Sci. Catal., 1994, vol.82, pp. 233-242.

6. Ivanov A.A., Yabrov A.A., Karnatovskaya L.M., Petuchova N.A., Chaikovskii S.P. o-Xylene oxidation to phthalic anhydride over unsteady state of the catalyst. React. Kinet. Catal. Lett., 1997, nn.1, pp.75-82.

7. Pan H.Y., Minet R.G., Benson S.W. and Tsotsis T.T. Process for converting chloride to chlorine. Ind. Eng.  Chem. Res., 1994, nn.9, P. 2996-3003.

8. Kuznetsov Yu.I., Mahotkin O.A., Slinko M.G. Modeling of the chemical process in a fluidized bed under the catalyst usteady-state. Doklady Akademii Nauk USSR, 1972, no. pp.145-148. (in Russ.).

9. Pokrovskaya S.A, Slinko M.G., Sheplev V.S. Analysis of a chemical processes in fluidized bed with the catalyst usteady-state. Doklady Akademii Nauk USSR, 1975, no.1, pp.157-160 (in Russ.).

10. Pokrovskaya S.A, Sheplev V.S., Slinko M.G.  Estimation of the conditions of a catalytic reaction run stationarity in fluidized bed. Doklady Akademii Nauk USSR, 1979, no.3,  pp.669-672 (in Russ.).

11. Mahotkin O.A., Ostrovsky N.M., Kuznetsov Yu.I, Slinko M.G. Influence
of the oxygen transport in the volume of the solid phase on its state in the fluidized bed.

Doklady Akademii Nauk USSR, 1979, vol.249. p. 403-406 (in Russ.).

12. Evenchik A.S., Makhlin, VA, Timoshenko V.I., Slinko M.G. About the quasi-stationarity of the heterogeneous catalytic reaction in the reactor with upward flow. Doklady Akademii Nauk USSR, 1982,  no.5, pp.1209-1212 (in Russ.).

13. Matros Yu.Sh. Forced unsteady-state processes in heterogeneous catalytic reactors. Can. J. Chem. Eng., 1996, no.3, pp. 66-578.

14.  Ross G.R., Hudgins R.R., Silveston P.L The Fisher-Tropsh synthesis over a ruthenium       catalyst under composition cycling. Can. J. Chem. Eng., 1987, vol.65, pp.958-965.

15. Ivanov E.A., Ivanov A.A., Reshetnikov S.I. Increase of selectivity for the reactions of partial oxidation of a hydrocarbons in the dual-reactor system. Theoretical Foundation of Chemical Engineering., 1998, no.5, pp.530-535.

16.  Reshetnikov S.I, Ivanov A.A., Gaevoi V.P., Sadovskaya E.M, Pinaeva L.G., Ivanov E.A., Balzhinimaev B.S. Multiplicity of regimes in a dual-reactor system with the catalyst circulation in oxidation of o-xylene into phthalic anhydride. The International Conference on Chemical Reactors “Chemreactor-13”, Novosibirsk, 1996. Abstracts,  pp.5-8.

17.   Reshetnikov S.I, Ivanov A.A., Gaevoi V.P. Mathematical simulation of the oxidation of

ortho-xylene to phthalic anhydride in a fluidized catalyst bed. Kinetics and Catalysis. 2009, no. 2, pp. 344-350.

18.   Gaevoi V.P. Analysis of mathematical models of processes in fluidized bed under the catalyst usteady-state. In the book. "Mathematical modeling of catalytic reactors". Novosibirsk: Nauka, 1989. pp. 75-84 (in Russ.).

19. May W.G. Fluidized-bed reactor studies. Chem. Eng. Progr., 1959. vol. 55, pp. 49-56.

Aromatization process modeling C5 hydrocarbons in a shelf fixed bed reactors

Balaev Alexandr Vsevolodovich

Doctor of Science (Chemistry), a professor of Ufa State Oil Technical University at the Department of petrochemical and chemical technology.

Address: 450062, city Ufa, Kosmonavtov street, 1.

E-mail:  avbalaev@gmail.com

Vyatkin Yurij Leonidovich

Candidate of technical Sciences, associate Professor of Russian chemical-technological University named after D.I. Mendeleev at the Department of General chemical technology

Address: 125047, Moscow А-47, Miusskaya square, 9

E-mail:  yuris-vtk@mail.ru

Key words: aromatization reaction, kinetic equations, reaction rate constants,  mathematical model, computational experiment, adiabatic fixed bed reactor

Abstract. Kinetic model of the catalytic conversion wide fraction of C2-C5 hydrocarbons to desired products: benzene, toluene and xylenes was developed. For 18-stage scheme of transformations, inversed kinetic task was solved and  kinetic parameters,  described experimental data in the limits of quantities analysis inaccuracy were determined. Simulation process for four-and three-fixed bed reactors was realized. The yields of the benzene, toluene and xylenes, with variations of pressure, temperature and volume of the catalyst were calculated by means of computer experiment. It was showed that the maximum yield of target products is achieved in four- layer reactor with the catalyst distribution in layers in the proportion of 1:1:1:2.

References

- Кutepov B.I., Belousova О.Yu. Aromatizaciya uglevodorodov na

pentasilsoderzhaschih ratalizatopah. // М.: Chimiya, 2000. 95s.

- Lukyanov D.B., Gneep N.S., Guisnet M.R. Kinetic modeling of ethane and

propene aromatization over HSM-5 and  GaHSM-5. // Ind. Eng. Chem., Res.

1994. V.33. P.223-234.

- Jana A.K., Rao M.S. Selective aromatization of C3- and C4- parafins over

encilite catalysts. 2. Kinetics of n-butane aromatization. // Ind. Eng. Chem.,

Res. 1993. V.32. P.2495-2499.

- Rid R., Prausnits J, Sherbud Т. Svoistva gazov i gidkostej. // L.: Chimiya,

1982. 592 s.

Computer assistant to technologist

in a process of propylene polymerization

Ostrovskii Nickolay Mikhailovich

Hipol a.d.,

Director of Quality and Development

Professor,  Doc. Sci.

Gračački put b.b.,  25250 Odžaci,  Serbia

Tel.: +381-25-464-760,  Fax:  +381-25-464-702,

e-mail:  nikolaj.ostrovski@hipol.rs

Key words: computer assistant to technologist; Propylene polymerization

Abstract.  In this paper, the software named Computer Assistant to Technologist (CAT) for the process of propylene polymerization is presented, which was created in a software environment of Excel - VBA. Such an approach was chosen in assuming that every chemical engineer is a master of Excel as yet, and can create and develop a personal CAT according to process features and personal computer-based experience. The structure of CAT and the simplified model of the process under steady-state regimes are presented. Model and program were used for estimation of maximum performance of the reactor; for designing of closed cooling system; and for simulation of three-reactor system (2+1) that gives a possibility to redouble the capacity of reactor unit.

### References

- Ostrovskii N.M., Kenig F. About mechanism and model of deactivation of Ziegler–Natta polymerization catalysts. // Chem. Eng. Journ. 2005. V. 107, No. 1. P. 73-77.

- Ostrovskii N.M., Stoiljkovic D.  Evaluation of the effect of reaction and mass transfer on the growth of polymer particles in olefin polymerization. // Theor. Found. Chem. Eng. 2011. V. 45, No. 1. P. 40-52.

- Reid R.C., Prausnitz J.M., Sherwood T.K. The properties of gases and liquids. McGraw-Hill, New York, 1977.

- Pavlov K.F., Romankov P.G., Noskov A.A.  Primery i zadachi po kursu processov i apparatov himicheskoy tehnologii. L.: Himiya, 1981.

- Chernobylskii I.I., Haytin B.Sh.  Polimerizacionnye apparaty. Kiev. Tehnika, 1968.

- Strenk F.  Peremeshivanie i apparaty s meshalkami. L.: Himiya, 1975.

- Perry’s Chemical Engineers’ Handbook, McGraw-Hill, New York, 1984.

- Ostrovskii N.M., Fekete L. Process dynamics in slurry polymerization. / 20-th Int. Conf. on Chemical Reactors, "CHEMREACTOR-20", Dec. 2012, Luxemburg. Abstracts.

- Ostrovskii N.M. Drying of polymer powder in fluidized bed. Modeling of multizone dryer. // Chemical Industry. 2014. V. 68, No. 4. (in Press - DOI:10.2298/HEMIND131016007O).